## Slide 1
32G mentor-mentee
  First year M&M review
Nov, 27 - 2021
Khang tran
Backend 23 group
Renesas Electronics Corporation

## Slide 2: Agenda
Introduction Page 03
Achievement and detail status Page 05
Target in 2nd year Page 10
Difficulties and solutions Page 12
Q&A Page 13
Appendix Page 14
About Content of presentations. There are 6 part

## Slide 3: 1. Introduction 1.1 Mentor –mentee
MENTOR:
Name: Nguyen Le Minh Hac
Generation: 24G
Code: 1804
Group: Backend 23
MENTEE:
Name: Tran Dang Vinh Khang
Generation: 32G
Code: 2676
Group: Backend 23
firstly! Introduction: My name is Khang from BE23 and my mentor is Nguyen Le Minh Hac Who guide to me during to the past year.

## Slide 4: 1. Introduction 1.2 Mentor –mentee SYSTEM
Come to mentor-mentee system My Purposes in one year later:
I will Improve the communication between mentee and mentor.
Beside that, I can catch up the skill level of mentor and other experienced team members.
I will increase the productivity instead of supporting from Mentor. (Reduce the support time and increase the productivity of mentee.)
Finally, Meet the requirement of real projects.
About Target:
I will Improve soft skills such as: communication, documentation, report, mindset, etc…
Must achieve level 3 for technical skill after 2 years.
On job training and complete at least 2 years.

## Slide 5: 2. Achievement and detail status 2.1 Overview: technical skill
2020, Oct
2021, Jun
2021, Dec
Focus on MCU product
MCU Product
U2A6 Project:
I can Design analog PG for analog HMs (PLL modules, AWOVDC, HOCOVDC, HOCO, LOCO, MainOSC, THS).
Verify open, short, DRC for analog PG.
Execute and fix ESD resistance by HSSC tool.
Building HSSC environment automatically to check resistance.
Develop script to generate report of RedHawk result automatically.
U2B6 Project:
Implement for analog signal wiring full chip (analog module FLI, analog module SYS,AD0/1/2, ADS,RDC,THS, FCMP).
Verify LVS (ICC2), DRC, StarRC, Eagle.
MCU Product
This is a secondlly: the achievement and detail satatus, and there are 2 technical skill: Include PG design and analog implementation. this is the terget that my mentor defind during1 year. About the detail task during 1 year, I did two project in the MCU Product: first the U2A6 project: I have a knowledge of my task as: the second U2B6 project: This is brirly information about 2 project that I completed them in the first year

## Slide 6: 2. Achievement and detail status 2.2 PG design and verification
Achievement of the U2A6 project :
This is detail information about achievement in the U2A6 project:
First I achievement Understanding specification document of analog hard macro.
Can create some script (TCL) in order to make routing more convenient.
Can use HSSC environment to analyze and measure resistance value.
Having the knowledge how to reduce resistance in order to save routing resource that contribute Floorplan target and satisfy design constraints.
The picture in the left handside:This is patterns I base on the specification and routing as instruction, and there is no more spcing so I should route as narrow as possible in order to leave resource for other HM and right handside It’s show P2P measurement and result resistance.

## Slide 7: 2. Achievement and current status 2.2 PG design and verification
Achievement of the U2A6 project:
Come to HSSC environment Basing on my knowledge about HSSC verification flow. So, I have built the automatically HSSC environment from ICC2 tool to measurment resistance.(one of Kaizen) Because Before HSSC resistance environment is measured by manual from getting GDS merge 1, preparing start point and end-point, run measurement, and generating the report. Now, my environment can automatically run from collect P2P coordinate and export into HSSC data and also define PG net name and GDS file automatically in HSSC P2P data after that finished HSSC execution, the env will be exported excel file result, Based on HSSC result.That is From num 1 to num 2.However num 3 is still work manual. In the future I will con….

## Slide 8: 2. Achievement and detail status 2.2 PG design and verification
Achievement of the U2A6 project:
About the Redhawk verification, I Base on the Python language skill to develop scripting environment in order to auto run all checker generate report of RedHawk automatically and feedback to PG designer to improve RedHawk result. (One of Kaizen).
Before that,when receive environment of REL from Jappan,Not only all run the steps manually but also colect data result by fill in excel file. So, I improve by building environment to run all the checker. After that the all of checker result are availible, and export excel file for all redhawk result of all checker. That mean Each sheet contain measurement of resistance or current density result. Actually! script can automatically judge.
Question: I don’t know fix redhawk result, I just only know the redhawk flow and I use python skill in order to script environment auto run and generate report. My achievement when achieve Build environment and generate reprot.

## Slide 9: 2. Achievement and detail status 2.3 Analog implementation
This is detail information about Achievement of the U2B6 project:
I Contribute to reduce chip dead space by design analog wiring with total area as least as possible.
In the FLI area, In order to reduce dead space, So I have to lessen widh of metal as much as posible.
Can use Custom Compiler tool to support faster routing after that we export the pattern from Custum Compier to ICC2 and reduce a lot of manual analog routing
Can calculate and estimate resistcance/capacitance to route pattern which satisfiles the constraint:
  To reduce capacitance: use high layer, extend shield X3 or more, jump shield.
  To reduce resistance: Increase metal width, routing on multiple layer and stack VIA.
Understanding how to make suitable shielding for Analog nets.
  The Purposes of suitable shieding for Analog net sensitive and has high impedance, frequency, speed in order to prevent noise between analog nets and other nets, that cross or run parallel analog nets
Understanding how to fix eagle verification. This is result of analog signal patterns

## Slide 10: 3. Target 2nd year 3.1Target: Technical skills
No | Skill items | 1st year result | 2nd year plan (Sep 2021 – Jun 2022)
1 | PG design and verification. | 2 | 3
2 | Analog implementation | 2 | 3
3 | Physical Verification | 1 | 2
Target:
Must achieve level 3 for with target as define in advance.
Deal with task with supporting as less as possible from Mentor.
Can instruct younger engineer in my responsible segment.
Come to number 3 of content about target 2nd year

## Slide 11: 3. Target 2nd year 3.2 Target: Soft skills
Soft skills | Target
Communication | Can report problem in group and can negotiate with group member.
Task management | Can estimate schedule and make action to keep schedule

## Slide 12: 4. Difficalties and solutions
Difficulties
  I work with New tool, new environment, it’s rather difficult to get familiar
  Lack of experienced about Physical verification
My Countermeasures
  Trial previous design to understand tool’s behaviors
  Investigate the document, discuss with mentor to receive the guidance. Trial legacy data to understand physical verification
Come to number 4 of content: Difficalties and solutions

## Slide 13: 5.

## Slide 14: 6. APPENDIX 6.1 Definition of skill level
Role Level | Definition | Skill Level | Definition
1 | Can do the job with help from others | 1 | Has no knowledge, no experience
2 | Can do the job without any help, if it is within certain degree of difficulty. | 2 | Can do the job with help from others.
3 | Can do any given job without any help | 3 | Can do any given job without any help
4 | Can make his/her experiences into knowledge for others, and apply them to improve the job, as well as train juniors. | 4 | Can analyze and improve/refine the job
5 | Can lead within the company | 5 | Can develop new technologies, and can apply advanced method, and can direct technologies including advanced method.
6 | Can be recognized in the market |  | 
7 | Can lead the market |  | 

## Slide 15
Renesas.com